## Slide 1
NVIDIA BLACKWELL
Architecture
The Next Generation of AI Computing
GPU ARCHITECTURE
AI ACCELERATION
COMPUTER ENGINEERING
Seminar Presentation • Diploma Computer Engineering

## Slide 2
1. Why AI Needs New Hardware
• Modern AI models require enormous parallel computation.
• Moving data between compute and memory is a major bottleneck.
• Specialized accelerators can perform AI operations much more efficiently than general-purpose CPUs.
• Blackwell is designed around this AI-scale computing problem.
AI MODELS
MASSIVE PARALLELISM
MEMORY BOTTLENECK
NVIDIA Blackwell Architecture • Seminar | 2

## Slide 3
2. CPU vs GPU
• CPU: a small number of powerful, general-purpose cores.
• GPU: many parallel processing units optimized for throughput.
• Neural networks contain huge numbers of parallel matrix operations.
• GPU architecture maps naturally to these workloads.
CPU
GPU
AI WORKLOAD
NVIDIA Blackwell Architecture • Seminar | 3

## Slide 4
3. NVIDIA GPU Evolution
• NVIDIA architectures have evolved from graphics-focused GPUs to general accelerated-computing platforms.
• Major data-center generations include Ampere, Hopper and Blackwell.
• Each generation adds more AI-focused hardware and faster interconnects.
• Blackwell is the successor to Hopper for the newest generation of AI computing.
AMPERE
HOPPER
BLACKWELL
NVIDIA Blackwell Architecture • Seminar | 4

## Slide 5
4. What is Blackwell?
• Blackwell is an NVIDIA GPU architecture introduced for generative AI and accelerated computing.
• Blackwell-architecture GPUs use 208 billion transistors.
• The data-center Blackwell GPU uses two dies connected by a 10 TB/s chip-to-chip link.
• The architecture targets training, inference and large-scale AI systems.
208B
TRANSISTORS
2 DIES
10 TB/s
NVIDIA Blackwell Architecture • Seminar | 5

## Slide 6
5. Inside a Blackwell GPU
• Compute: Streaming Multiprocessors execute massively parallel workloads.
• Tensor Cores accelerate matrix/tensor operations used by AI.
• High-bandwidth memory feeds data to the compute engine.
• High-speed interconnects let multiple GPUs work as a larger system.
SM
TENSOR CORES
HBM
NVLINK
NVIDIA Blackwell Architecture • Seminar | 6

## Slide 7
6. Tensor Cores
• Tensor Cores are specialized hardware for matrix and tensor math.
• They are central to AI training and inference acceleration.
• Blackwell introduces fifth-generation Tensor Cores.
• New precision formats help increase throughput while controlling memory use.
5th GEN
TENSOR CORES
MATRIX MATH
NVIDIA Blackwell Architecture • Seminar | 7

## Slide 8
7. FP4 & Transformer Engine
• Blackwell adds FP4 AI capability using microscaling techniques.
• Lower numerical precision can reduce memory and increase throughput.
• The second-generation Transformer Engine dynamically manages precision and scaling.
• The goal is faster AI computation while maintaining useful model accuracy.
FP4
MICROSCALING
TRANSFORMERS
NVIDIA Blackwell Architecture • Seminar | 8

## Slide 9
8. High-Bandwidth Memory (HBM)
• AI accelerators constantly move large amounts of model and activation data.
• HBM provides very high memory bandwidth close to the GPU.
• More bandwidth helps keep compute units supplied with data.
• Memory bandwidth is as important as raw compute for many AI workloads.
HBM
HIGH BANDWIDTH
LOW LATENCY
NVIDIA Blackwell Architecture • Seminar | 9

## Slide 10
9. NVLink: Connecting GPUs
• Large AI models often need many GPUs working together.
• Fifth-generation NVLink provides high-bandwidth, low-latency GPU communication.
• NVLink Switch creates large GPU communication domains.
• This reduces communication bottlenecks in distributed AI systems.
GPU 1
NVLINK
GPU 2
GPU 3
NVIDIA Blackwell Architecture • Seminar | 10

## Slide 11
10. GB200 Grace Blackwell Superchip
• A GB200 Grace Blackwell Superchip combines one Grace CPU with two Blackwell GPUs.
• NVLink-C2C provides a high-speed connection between CPU and GPUs.
• It is designed for data-center AI and high-performance computing.
• Multiple superchips can be assembled into rack-scale systems.
GRACE CPU
2 × BLACKWELL
NVLINK-C2C
NVIDIA Blackwell Architecture • Seminar | 11

## Slide 12
11. Blackwell at Rack Scale
• GB200 NVL72 connects 36 Grace CPUs and 72 Blackwell GPUs.
• The system uses fifth-generation NVLink to create a large GPU communication domain.
• Liquid cooling supports the high power density of the rack.
• This demonstrates that modern AI computing is a system-level engineering problem.
36 CPUs
72 GPUs
130 TB/s NVLINK
NVIDIA Blackwell Architecture • Seminar | 12

## Slide 13
12. Blackwell and Generative AI
• LLM training: learning model parameters from huge datasets.
• LLM inference: generating responses after a model is trained.
• Mixture-of-Experts models can activate only selected expert networks.
• Blackwell combines Tensor Cores, Transformer Engine, memory and interconnect technologies for these workloads.
TRAINING
INFERENCE
MoE / LLM
NVIDIA Blackwell Architecture • Seminar | 13

## Slide 14
13. Blackwell vs Hopper
• Blackwell succeeds Hopper as NVIDIA's newer data-center GPU architecture.
• Blackwell introduces a second-generation Transformer Engine and FP4 AI capability.
• Blackwell uses a two-die design connected by a 10 TB/s chip-to-chip link.
• The architecture also advances GPU-to-GPU communication with fifth-generation NVLink.
HOPPER
BLACKWELL
FP4 / NVLINK
NVIDIA Blackwell Architecture • Seminar | 14

## Slide 15
14. Power, Cooling & Reliability
• More computation creates more heat and power-management challenges.
• High-density AI systems increasingly use liquid cooling.
• Blackwell also includes hardware security and a dedicated RAS Engine for resilience.
• Thermal, electrical and reliability engineering are critical alongside chip design.
POWER
LIQUID COOLING
RAS
NVIDIA Blackwell Architecture • Seminar | 15

## Slide 16
15. Real-World Applications
• Generative AI and large language models.
• Scientific computing and engineering simulation.
• Data analytics and enterprise AI.
• Robotics, autonomous systems and advanced computer graphics.
GEN AI
HPC
ROBOTICS
GRAPHICS
NVIDIA Blackwell Architecture • Seminar | 16

## Slide 17
16. Key Takeaways
• Blackwell is more than a faster GPU: it is an architecture for AI-scale systems.
• Tensor Cores accelerate AI math; HBM supplies data; NVLink connects GPUs.
• Advanced packaging and rack-scale design are becoming essential for AI.
• Future computing will increasingly combine specialized hardware, memory and high-speed interconnects.
COMPUTE
MEMORY
INTERCONNECT
SYSTEM
NVIDIA Blackwell Architecture • Seminar | 17

## Slide 18
References
• NVIDIA — Blackwell Architecture (official architecture overview)
• NVIDIA — GB200 NVL72 and Grace Blackwell Superchip
• NVIDIA — Blackwell / CUDA Tuning Guide
• NVIDIA — Tensor Cores and Blackwell Transformer Engine
• NVIDIA — Blackwell GPU Architecture technical documentation
Source links are provided in the accompanying seminar notes/documentation.
NVIDIA Blackwell Architecture • Seminar | 18

## Slide 19
THANK YOU
Questions?
NVIDIA BLACKWELL ARCHITECTURE
NVIDIA Blackwell Architecture • Seminar | 19